ADS1299 Key Parameters and Equations
Basic Definitions:
Output Data Rate (fDR): The rate at which samples (readings of the analog input signal) are outputted from the ADC. The datasheet often interchanges output data rate with *sample rate* which can get confusing sometimes. Note that this is different from the rate at which the ADC samples the analog signal (modulator frequency)
Modulator frequency (fMOD): The frequency at which the modulator samples the input. This is what we all normally refer to as the sampling rate.
Master Clock frequency (fCLK): The frequency of the clock at which the ADS system. The chip supports the use of an external oscillator (which is fed through the CLK pin) or a built-in internal oscillator (which we will be using for the sake of simplicity).
ADC Bits per Sample: The number of bits used to represent one sample or reading.
ADC Resolution: The number of discrete levels a ADC can quantize an analog signal.
Number of quantization levels = 2n where n is the bits per sample

In this figure, the bits per sample is 3, and the resolution is 23 = 8 levels
The resolution (24) does not actually define the voltage difference between two quantization levels. How much voltage one bit (or 1 LSB) of the 24-bit data represents is calculated by Equation 8 on page 38 of the datasheet. It is a function of your reference voltage (VREF) and PGA gain, both of which can be set or programmed.
Frequency and Period: The relationship between the period and frequency is: Period = 1/Frequency. For all the frequencies mentioned above (fMOD, fCLK, etc.) the datasheet also references tMOD, tCLK, etc., which are just the periods of the corresponding frequency.

Equations
fMOD = fCLK / 2
1 LSB = (2 × VREF / Gain) / 224

Default Parameters
fCLK = 2.048 MHz (internal oscillator frequency)
fMOD = 1.024 MHz
VREF = 4.5 V (This is the default)
Gain = 24
1 LSB = 0.0223 uV (microVolts)
Note: The need to oversample at such a high sample rate is because of the need to minimize the noise (quantization error) that is inherently produced when you quantize a signal that can take on infinite continuous values to a discrete number of levels. If you’re interested, the following links explain the Delta-Sigma ADC technology which is the core of why the ADS1299 is so good:
- An explanation of quantization noise and how Delta-Sigma ADCs solve these problems:
  - https://www.maximintegrated.com/en/app-notes/index.mvp/id/1870
- How TI implements its Delta-Sigma ADC system:
  - Part 1: http://www.ti.com/lit/an/slyt423a/slyt423a.pdf
  - Part 2: http://www.ti.com/lit/an/slyt438/slyt438.pdf
fDR: 250 SPS to 16 kSPS (samples per second)
The OpenBCI runs at 250 SPS which is the slowest data rate offered because of certain bottlenecks in their design, like the RFduino which uses a serial link which has a max baud rate of 115200 bits per second.
Data Format:
One data packet outputted by the ADS consists of a 24 status bits and 24 bits * 8 channels for a total of 216 bits per reading. This means that one reading of data consists of 216 bits.
Explanation of OpenBCI packet format: https://github.com/OpenBCI/OpenBCI-V2hardware-DEPRECATED/wiki/Data-Format-for-OpenBCI-V3
ADS1299 Control Registers
Default Settings:
ID:
REV_ID: xxx
DEV_ID: 2‘b11
NU_CH: 2‘b10 (For ADS1299)
CONFIG1: Configures daisy chain, clock and data rate.
!DAISY_EN: 1‘b0 - Daisy chain mode
CLK_EN: 1‘b0 - Oscillator clock output disabled
DR: 3‘b110 - Output data rate = fMod / 4096 = 250 SPS
CONFIG2: Configures test signal
INT_CAL: 1‘b0 - Test source = external
CAL_AMP: 1‘b0 - Test signal calibration amplitude =	(VREFP - VREFN) / 2400
CAL_FREQ: 1‘b0 - Test signal frequency = Pulsed at fCLK / 2^21
CONFIG3:
!PD_REFBUF: 1‘b0 - Power down internal reference buffer
BIAS_MEAS: 1‘b0 - Disables BIAS measurement
BIASREF_INT: 1‘b0 - BIASREF is fed externally
!PD_BIAS: 1‘b0 - BIAS buffer is powered down
BIAS_LOFF_SENS: 1‘b0 - BIAS sense function is disabled
BIAS_STAT: 1‘b0 - BIAS lead-off status -> BIAS is connected