ADS1299 Key Parameters and Equations
Basic Definitions:
Output Data Rate (fDR): The rate at which samples (readings of the analog input signal) are outputted from the ADC. The datasheet often interchanges output data rate with *sample rate* which can get confusing sometimes. Note that this is different from the rate at which the ADC samples the analog signal (modulator frequency)
Modulator frequency (fMOD): The frequency at which the modulator samples the input. This is what we all normally refer to as the sampling rate.
Master Clock frequency (fCLK): The frequency of the clock at which the ADS system. The chip supports the use of an external oscillator (which is fed through the CLK pin) or a built-in internal oscillator (which we will be using for the sake of simplicity).
ADC Bits per Sample: The number of bits used to represent one sample or reading.
ADC Resolution: The number of discrete levels a ADC can quantize an analog signal.
Number of quantization levels = 2n where n is the bits per sample

In this figure, the bits per sample is 3, and the resolution is 23 = 8 levels
The resolution (24) does not actually define the voltage difference between two quantization levels. How much voltage one bit (or 1 LSB) of the 24-bit data represents is calculated by Equation 8 on page 38 of the datasheet. It is a function of your reference voltage (VREF) and PGA gain, both of which can be set or programmed.
Frequency and Period: The relationship between the period and frequency is: Period = 1/Frequency. For all the frequencies mentioned above (fMOD, fCLK, etc.) the datasheet also references tMOD, tCLK, etc., which are just the periods of the corresponding frequency.

Equations
fMOD = fCLK / 2
1 LSB = (2 × VREF / Gain) / 224

Default Parameters
fCLK = 2.048 MHz (internal oscillator frequency)
fMOD = 1.024 MHz
VREF = 4.5 V (This is the default)
Gain = 24
1 LSB = 0.0223 uV (microVolts)
Note: You may be wondering why the ADC modulator frequency (fMOD), when from what we know, most useful signals in the brain are nowhere near even the kHz frequency range, not to mention MHz. The need to oversample at such a high sample rate is because of the need to minimize the noise (quantization error) that is inherently produced when you quantize a signal that can take on infinite continuous values to a discrete number of levels. If you’re interested, the following links explain the Delta-Sigma ADC technology which is the core of why the ADS1299 is so good:
- An explanation of quantization noise and how Delta-Sigma ADCs solve these problems:
  - https://www.maximintegrated.com/en/app-notes/index.mvp/id/1870
- How TI implements its Delta-Sigma ADC system:
  - Part 1: http://www.ti.com/lit/an/slyt423a/slyt423a.pdf
  - Part 2: http://www.ti.com/lit/an/slyt438/slyt438.pdf
fDR: 250 SPS to 16 kSPS (samples per second)
The OpenBCI runs at 250 SPS which is the slowest data rate offered because of certain bottlenecks in their design, like the RFduino which uses a serial link which has a max baud rate of 115200 bits per second.
Data Format:
One data packet outputted by the ADS consists of a 24 status bits and 24 bits * 8 channels for a total of 216 bits per reading. This means that one reading of data consists of 216 bits.
Explanation of OpenBCI packet format: https://github.com/OpenBCI/OpenBCI-V2hardware-DEPRECATED/wiki/Data-Format-for-OpenBCI-V3